## Slide 1: STATUS OF PS APPARATUS
Lea Di Noto and Trento Group
Milano, 17-5-2012

## Slide 2
Buncher
Mu metal
electrode
Total lenght=120cm
108 mm
of external
diameter
coil
coil
Cryostat
General overview of the apparatus

## Slide 3
7 flange CF63 are overlooked at the sample
-2 for laser
-5 for channeltron or MCP,
for PbF2,
for microwave
Every plan of the flanges has four threaded holes to eventually attach some detector board
Special port
sample

## Slide 4
This is the special port as request by Zurich Group
It is a CF40 centered at distance 27 mm from the sample plane
Sample plane
There are 6 threaded holes to attach MCP system.
Two flange CF16 that can be useful
27 mm

## Slide 5: Time table
1. By a week the chamber will be in Trento
2. By fifteen days we will start the mounting of the optics.

## Slide 6
The chamber will be set-up on a support simulating the CERN’s one.
This will allow:
to construct mu-metal multi-shield without further design.
to built the support in Trento

## Slide 7
To design the PbF2 holders (we need the specific)
To construct the mu-metal shield (we need the dimensions of the necessary space for laser table and other boards attached to the chamber ports).
We need (and we have no money for) :
    Skroll pump
    Variac fro baking (we have to ask if we can use the CERN’s one)
To do